## Slide 1: Design elements and country experiences I: general design, auction procedure, conditions for participation
July 16, 2019

## Slide 2: Competitive procurement simulations
Participants understand competitive procurement, its procedure and key considerations in competitive procurement design as follows:
Understand how competitive procurement works in practice and the strategic considerations in competitive procurement by playing the role of a bidder
Become familiar with the concepts of winner’s curse, how it is perceived by bidders, and which design features can help mitigate the risk of winner’s curse
Appreciate how the sunk costs involved in participating in competitive procurement affect bidding strategies, and how design of competitive procurement be done considering sunk costs
Interactive Session

## Slide 3: Simulation A – the winner‘s curse
Based on Takon by Ehrhart, 2016
Competitive procurement for a renewable energy project
The bidder has difficulty in estimating his costs (symbolized by a can with cash). Each bidder estimates the amount of the cash in the can and notes it on a piece of paper. Cover the piece of paper.
Static sealed bid auction – all bidders hand in their bids at the same time
Each bidder decides on a bid price and writes it on a piece of paper.
Announcement and evaluation of the results
Interactive Session

## Slide 4: Introduction to the problem of the winner‘s curse
Based on Takon by Ehrhart, 2016
Definition
  Auction bid price is less than the actual value of the good, which will result in a loss for the auction winner
Example
  Excessive yield or underestimated costs
Impact on bidders
  Often bidders tend to estimate the costs relatively well
  If bidders are guided by their cost estimates in their bid strategy, the bidder who underestimates costs wins the auction
Adequate bidding behavior
  Upward adjustment of the cost estimation in case of having a winning bid
  Adjustment of the bid where possible

## Slide 5: Simulation B – The problem of sunk costs – see seperate instructions sheet
Based on Takon by Ehrhart, 2016
Competitive procurement for a renewable energy project.
Static sealed bid auction – all bidders hand in their bids at the same time (write it on the paper and hand it in).
Each bidder will receive his individual project costs on a piece of paper. Bidders’ project costs are different.
Individual project costs consist of: already incurred costs (before the auction) and the remaining costs, which only accrue to auction winners.
Please write your bid on a piece of paper.
Start of the auction
Interactive Session

## Slide 6: Introduction to the problem of sunk costs
Based on Takon by Ehrhart, 2016
Definition
  Losses caused by sunk costs not only affect auction losers, but also the auction winner of an auction
Example
  Costs associated to project pre-development up to obtaining a permit
Bidding behavior
  Optimal bidding strategy is based only on residual costs and, if necessary, deducts sunk costs
Consequences due to sunk costs
  Lower acceptance or non-participation by bidders
  Risk of non-realization

## Slide 7: Focus on auctions: overview of competitive procurement design
  Lessons learned
  Adjustment of procurement design
Evaluation
  Drafting of required documents
  Market building
  Procurement conduction
  RfQ
  RfP and awarding of bids
  Contracting
  Monitoring of realization
Imple-mentation
  Institutional set-up
  What is auctioned
  Procurement procedure
  Conditions for participation
  Enforcement of obligation
  Rights for awarded projects
Procurement design
  Market size
  Pre-developed project
  Market players
  Technology cost
  Project development & operation
  Existing regulations & incentives
Market & regulatory analysis
  Policy goals
Target definition

## Slide 8: Overview of different design elements and functions
Institutions
Auction regulation, design, implementation, contract off-taker
Rights & obligations of awarded projects
Provisions against off-taker, political and currency risk
Enforcement of obligations
Deadlines and penalties
Conditions for participation
Timing of the auction, technical requirements, financial bid bonds
Competitive procurement
procedure
Static vs. dynamic auctions, price, selection criteria, pricing rule, number of rounds
What is procured
Technology type, technology size, auctioned item (kWh, KW, budget), multi vs. single-item auction

## Slide 9: Site selection and preparation: benefits and challenges
Benefits
Lower admin. burden on government.
Site-specific risks mitigated through bidder-driven project development.
Challenges
Lower grid-compatible RE development in absence of locational signals.
Higher risks & costs of project development if uncertainty about project costs and timeline.
Bidder-site auction
15 MW
30 MW
Procured volume (e.g. 100 MW)
30 MW
25
MW
Bidder 1
Bidder 2
Bidder 3
Bidder 4
Auctioneer
Benefits
Grid-compatible RE development.
Lower risks & costs of project development if adequate quality.
Challenges
Higher admin. burden on government.
Reduced role of bidders in finding optimal site.
Risk of ‚faulty‘ site selection and preparation.
Government-site auction
Auctioneer
Project site
Selected & pre-developed
Bidder 1
Bidder 2
Bidder 3
Bidder 4

## Slide 10: Site selection and preparation: country examples
South Africa (with easier project development in Renewable Energy Development Zones - REDZ)
Mexico, Chile
Country examples
Bidder-site auction
15 MW
30 MW
Procured volume (e.g. 100 MW)
30 MW
25
MW
Bidder 1
Bidder 2
Bidder 3
Bidder 4
Auctioneer
Senegal’s Scaling Solar
Dubai/Abu Dhabi (UAE)
Morocco
Denmark offshore wind
Country examples
Government-site auction
Auctioneer
Project site
Selected & pre-developed
Bidder 1
Bidder 2
Bidder 3
Bidder 4

## Slide 11: Selecting permitting required before the auction is crucial
Planning
Approval process
Construction
Operation
Early auction:
RfQ stage
RfP stage
Project realization
Late auction:
RfQ stage
RfP stage
The inherent project risk is highest at the start of a project yet costs are still low.
If the auction takes place early in the project development process, i.e. before permits affecting the business case of a project (depending on the country: land lease, grid connection) are secured, there is a risk projects are delayed or cancelled.
Conducting sufficient site feasibility studies and procuring key permits before the auction allows bidders to better estimate costs and makes projects more bankable. Feasibility studies should ideally be certified by an external agency e.g. research energy institute in Brazil.
Project failure risk declines with late auction.

## Slide 12: Conditions for participation: balance is the key
Financial capacity: Financial statements, letter of support lender,
Technical capacity: independently reviewed forecast energy sales reports
Site requirements: proof of land acquisition (title deed/notarial lease/unconditional land option)
Bidder qualification: South Africa
  Technical: Sunk costs
  All: Prohibitive barrier for (some) bidders
  Technical: Selection of projects with sufficient progress in planning
  Financial: Bidders with intention to realize
Conditions for participation
Planning
Approval process
Construction
Operation
Early auction:
RfQ stage
RfP stage
Late auction:
RfQ stage
RfP stage
Project realization

## Slide 13: Grid connection permit (1/II)
Type of grid connection permit required before the auction | No permit: increases risk of project delay or failure if uncertainty on when or if permit will be granted. In offshore wind auctions in Netherlands and Germany, grid connection permit is provided by the government (technology limited to specific sites) Preliminary permit (i.e. grid connection quotation/study): document from grid operator with indicative cost and timeline. South Africa: bidders request Cost Estimation Letter before bid submission. Proof of site control (letter from landowner) and initiation of environmental impact assessment need to be attached

## Slide 14: Environmental impact and social assessment: South Africa, Uganda
Uganda GET FiT - IFC standards
IFC Performance Standards on Environmental and Social Sustainibility were part of the pre-qualification requirements and bid evaluation Advantage: “gold standard” on social and economic impact assessments and mitigation schemes for infrastructure projects  requirement for funding IFC and other lenders. Disadvantage: considerable costs on developers  compliance viable for few projects given auction timeline
South Africa – environmental standards
Renewable Energy Development Zones introduced in 2016 (for Bid Window 5) Strategic environmental assessments (SEA) are performed prior to bidders’ site selection. RE projects and the associated grid infrastructure to be developed with a simplified environmental authorization. RE deployment under the auction is not exclusive to the zone

## Slide 15: Be careful not to overburden bidders: In Mexico, EDF needed to interact with 13 agencies